Engine Run up
read the displays/indicators at full throttle

        Min Max
RPM 1550 1650
Oil pressure 3 kg/cm2 6 kg/cm2
Oil temp 35 c 85 c
Fuel pressure 0.2 kg/cm2 0.22 kg/cm2

dropout must not be more than 50 rpm on single magneto operation

Minimum speed at level flight and with max. load is 50km/h (27 KCAS) with engine powered on!

In the following table are the minimum distances in meters and Doppelschritten before obstacles.
The values represent the ones which skilled pilot may achieve at a take off at zero wind from a flat good grass runway and a total weight of 1260 kg (main-tank maximum, two crew, with the FT-device) routes lowest achievable.

        | height of the obstruction in m:
        | 8 | 10 | 15 | 20
        Meter | 135 | 150 | 175 | 200
Doppelschritte | 90 | 100 | 117 | 133

(one Doppelschritt is 1.482 Meters)

Cruise speed 150 km/h (80 KCAS) at 1800 rpm
Minimum safe speed 70 km/h (38 KCAS) at 1300 rpm

Maximum speed:
with full flaps lowered 120 km/h (65 KCAS)
recovered with flaps 256 km/h (143 KCAS)